## Slide 1: Fundamentals of Bronchoscopy: ENDOBRONCHIAL BIOPSY
BI, All Rights Reserved, 2017
www.Bronchoscopy.org
5/10/17

## Slide 2: Strategy and planning Techniques and results Response to complications
bronchoscopy.org

## Slide 3: When to perform endobronchial biopsy
BI
Visible airway mucosal abnormalities
Visible airway nodules or masses
In case of suspected sarcoidosis (even if airway mucosa appears normal)
In case of abnormal autofluorescence to diagnose intraepithelial lesions (dysplasia, metaplasia, carcinoma in-situ)

## Slide 4: Training is essential in order to
BI
  Learn proper techniques and indications
  Avoid procedure-related complications.
  Learn to protect the equipment and the patient
    To obtain adequate tissue for diagnosis
    To avoid damaging the working channel
    To avoid excess patient discomfort (cough, anxiety, shortness of breath).
    To avoid bleeding, that might also prompt cough and patient agitation.

## Slide 5: Endobronchial Biopsy
BI
Indications
  Visible intraluminal or mucosal abnormality
  Suspected Sarcoidosis (even if mucosa appears normal)
  Early lung cancer detection (based on findings of autofluorescence and other imaging modalities)

## Slide 6: Biopsy instruments
BI
Small reduction in bleeding using hot forceps: 39 patients with 6 biopsies each (Eur Respir J 2007; 29:108-111
Forceps with spike can be used to anchor forceps on lesion.
Open cup
Alligator (serrated)

## Slide 7: Examples of biopsy forceps
BI
Serrated forceps and cup forceps
Cup forceps with central tooth
Forceps may be single use or reusable

## Slide 8: Endobronchial biopsy: Electrocautery forceps can be useful
BI
Hot biopsy forceps in the diagnosis of endobronchial lesions
  39 patients with 6 biopsies each (hot and cold)
  Pathologic concordance between hot and cold biopsies was 92.5% and 87% (2 pathologists)
  Small reduction in mild bleeding episodes with hot forceps (at 40-60-80-100 W)
  Authors: routine use not warranted – can use as cold with set up for EC if significant bleeding occurs
(from Olympus America)
  Eur Respir J 2007; 29:108-111

## Slide 9: Biopsy techniques
BI
Approach
Open forceps
Close and biopsy
Engage as much tissue as possible
Keep scope as close to target tissue as possible
May feel tugging sensation as forceps retracted

## Slide 10: Obtaining the best specimen possible
BI
Use forceps with central tooth, especially if lesion is along lateral wall of trachea or bronchi.
Obtain deep submucosal biopsies to increase yield for small cell carcinoma, Amyloidosis, Sarcoidosis and other infiltrating processes.
Get close to the target area with the bronchoscope.
Click here for video

## Slide 11: Deep, submucosal biopsy
A
B
Wedge the forceps onto the target area, push on the forceps to dig into the tissues, then close forceps

## Slide 12: Use cup forceps or forceps with central tooth to anchor forceps onto lateral wall lesions
Grade 4 Squamous Cell Carcinoma in LMB

## Slide 13: Yield of endobronchial biopsy
BI
Respir Med 1998;92:1110-5
  82% yield for malignancy if disease visible
  Best yield probably with combination of brushings, washings, and biopsy material
  Optimum sequence of procedures unknown
Thorax 1982;37:684-7
  4-5 biopsy samples from visible lesion achieves at least a 90% positive rate for malignancy2
  EBNA and TBNA probably superior to forceps biopsy in submucosal and peribronchial carcinoma

## Slide 14: Diagnosis of Lung Cancer
BI
Endobronchial Biopsy:
3-5 biopsies for 90 – 100 sensitivity in lung cancer
Variable yield 67 – 100% d/t:
  Sampling error,
  crush artifacts, surface necrosis, inadequate tissue
  submucosal disease
  extrinsic compression

## Slide 15: Endobronchial biopsy: Biopsy or wash first ?
BI
Yield: Effect of different bronchial washing sequences on diagnostic yield in endoscopically visible lung cancer
  75 patients underwent washing pre/post endobronchial biopsy and brushing
Arch Bronconeumol. 2006;42(6):278-82

## Slide 16: Endobronchial biopsy: Sarcoidosis
BI
Yield: Endobronchial biopsy (EBB) for sarcoid
  34 patients underwent TBBX and EBB
  If airways appeared normal – biopsies from main and a secondary carina
  EBB positive in 62%
  TBBX positive in 59%
  Addition of EBB increased yield by 21%
  EBB positive in 30% of patients with normal airway
  No additional complications from EBB
CHEST 2001;120:109-114

## Slide 17: False negatives do occur
BI
Due to necrotic surface or if process 2-3 mm below mucosal surface
  Absence of blood suggests necrosis
Therefore, take biopsies until the core is reached

## Slide 18: Case example: 72 year old with hemoptysis
BI
72 year old, non-smoker female with Diabetes, on 50 mg/d Prednisone presents with hemoptysis, fever and wheezing.
ANCA negative
ANA negative
PPD negative

## Slide 19: Your diagnosis is ?
BI
Endobronchial Wegener's
Endobronchial tuberculosis
Tracheobronchitis from inflammatory bowel disease
Squamous cell carcinoma
Endobronchial Cryptococcosis

## Slide 20: The answer is Endobronchial Cryptococcosis
BI
Rare, Incidence unknown
Presentation: Mass, plaque, sub-mucosal infiltration, Ulcer
From: JOB 2005; 12(4): 236-238

## Slide 21
BI
Fungal elements

## Slide 22: Complications of endobronchial biopsy
BI
Chest 1991;100:1141-7
  Profuse bleeding less likely than in Transbronchial biopsies
  Increased risk in Uremia, pulmonary hypertension, liver disease, thrombocytopenia and immunosuppression
  Superior vena cava syndrome – no literature on risk of biopsy bleeding

## Slide 23: Complications of endobronchial biopsy
BI
Thorax 2001;56(suppl I)i1-i21 British Thoracic Society guidelines
  Routine PT/PTT/platelet counts not indicated unless known risk factors
  It is unclear whether there is a safe level of INR or platelets

## Slide 24: www.Bronchoscopy.org
Prepared with help from Udaya Prakash M.D. (USA), Atul Mehta M.D. (USA), and Wes Shepherd M.D. (USA)